## Slide 1: Epileptic Monitoring Device
Final Design Presentation – December 4 2013
Mark Curran (CE), Rachel Kolb (BME), Kevin Pineda (BME), & Timothy Skinner (EE)
Primary Advisor: Dr. Brett BuSha Secondary Advisor: Dr. Ambrose Adegbege

## Slide 2: Agenda
Introduction
Problem/Solution
Design Overview
Electrodes
Headset Design
Signal Processing
Microcontroller
Android device/application
Budget
Timeline
Conclusion

## Slide 3: Introduction
Electroencephalography (EEG)- Test that measures and records electrical activity such as voltage fluctuations from ionic current flows within neurons of the brain
  Utilizes electrodes
  Used mainly for diagnosis of epilepsy
Epilepsy- Neurological disorder, characterized by
  Sudden, recurrent episodes of sensory disturbance
  Loss of consciousness or convulsions
  Abnormal electrical activity in the brain
Affects nearly 3 million Americans
  200,000 new cases per year
Cost upwards of $17.6 billion annually
Current treatment options
  Drug therapy e.g. anticonvulsant drugs
  Surgery

## Slide 4: Problem/Solution
Epileptic seizures- random occurrence, extremely difficult to accurately record outside hospital
  Time consuming and expensive for caretakers to constantly watch epileptic patients
  High risk if patient lives alone
  Cost of healthcare per person per year: $4000
Solution: Create an ambulatory epileptic monitoring device that triggers an alarm to a caregiver/physician when the patient is experiencing an epileptic seizure. Our device will store EEG information, and will be cost-effective, portable, and suitable for everyday use outside of a hospital for patients undergoing treatment for epilepsy.

## Slide 5: Design Overview
Electrodes
Isolation Amplifiers
Microprocessor
Battery and Signal Communication

## Slide 6: Electrodes
Number of electrodes directly related to spatial resolution of cortical potential distribution
Successful EEG readings have been taken using 4 electrodes
Clinically relevant EEG frequency band is 0.1 to 100 Hz, amplitudes along the scalp range 10-100 uV and vary by location

## Slide 7: Electrode Arrangement
10-20 International System
Electrode arrangements can vary from using 1 to >256 electrodes

## Slide 8: Electrodes for Design
5 electrodes at T3, C3, Cz, C4, and T4. Cz is reference
Cz is centrally located, not subject to asymmetrical electrical impulse propagation
Referential montage arrangement

## Slide 9: EEG Signals
Volume Conductor Effects
  Signal conductivity non-linear
  Cerebrospinal fluid
  Non-homogeneous compartments, lesions, directionally dependent tissues
Bio-electric activities
  Eye movement, muscle and cardiac activity
  Outside noise
  Inherent resistivity from skull and scalp
  1:80:1 brain, skull, scalp

## Slide 10: Type of Electrodes
Disposable or reusable
  Reusable
Wet or dry
  Wet
Shape
  Cup disc
Material
  Gold plated silver

## Slide 11: Emotiv EPOC Headset
Comparing non-epileptic EEG recorded by commercially available Emotiv EPOC headset and comparing to EMD recordings
All choices regarding electrodes were made with this comparison in mind
  Shape, size, placement, material, etc.

## Slide 12: Headset Design
Considerations:
Portability
Comfort
Lightweight
Electrode placement
Circuit storage
Aesthetically pleasing
Dimensions of average head, menton, and bizygomatic breadth:
  14.5 cm, 24.1 cm, and 13.9 cm.

## Slide 13: Manufacturing
Modeling Software: Solidworks
Easy to use
Powerful
Fabrication method: Objet30 Pro 3D Printer
Accuracy of .1 mm
Precise detail in design aspects
Material: VeroBlue
Finish: Matte

## Slide 14: First Prototype
Designed as one part
Hollow inside
“Cushion” to be placed around head for comfort
Bottom attachments for easy wire installation

## Slide 15: Bottom Attachment and Slot Mechanism

## Slide 16: Solidworks Prototype Assembly

## Slide 17: 3D Printed Headset Prototype
Printed in parts
Cost: $75

## Slide 18: Improvements
VeroBlue soft “fuzzy” texture, no need for “cushioning”
Shaped to fit around head - horseshoe shape
Slot mechanisms for electrode supports for easy assembly

## Slide 19: Final Design Headpiece

## Slide 20: Final Design Electrode Supports

## Slide 21: Solidworks Assembly

## Slide 22: Final Design Slot Mechanism

## Slide 23: Electrode Placement
Notes: Still a work in progress. Not finalized because we want to have the headset printed with the supports and fitted on the head properly before moving forward with electrode placement. Latch mechanism where a mock spring is created by bending the eeg electrode wire and putting it inside of a slit. A latch will then be used to fix it upon the head.

## Slide 24: Stress Analysis
Tests
Durability
Fracture/bending
Applied force: 50 N

## Slide 25: Stress Analysis
Force applied: 10 N

## Slide 26: Microcontroller
Arduino Pro Mini
Operating Voltage - 5V
Input Voltage - 5-12V
Atmel 328P – 16MHz
Digital I/O pins – 14 (6 can be PWM)
Pins Provide/Receive – 40mA

## Slide 27: Microcontroller (cont.)
Analog Input Pins – 8
ADC - 10 bit resolution at 15ksps
Programmed by using a FTDI cable
Coding – C++
Flash memory – 16KB (2 KB for boot loader)
SRAM – 1 kB
EEPROM – 512 bytes

## Slide 28: Microcontroller (cont.)
Open Source
Cross-platform compatible
Inexpensive
Very small dimensions, 18x33mm

## Slide 29: Epileptic Signal Characterization
There are many different methods of characterizing an epileptic EEG signal
The frequency of the brain wave could slow down.
There can be spike and sharp wave discharges when analyzing the amplitude over time.
There could be a different wave patterns occurring in the left temporal lobe, but nowhere else.
Large spike discharges that are widely spread over both hemispheres of the brain at the same time

## Slide 30: Epileptic Signal Characterization
Using the FFT (Fast Fourier Transform) we will be able to characterize any signal as either epileptic, non-epileptic, or non-determinant.
This is due to the 5Hz spike lasting longer than 5-10 seconds. This is what we will use to characterize seizure like signals

## Slide 31: Epileptic Signal Characterization

## Slide 32: Amplifier and Filter Circuit
Bio Amplifier
Circuit will perform voltage shifting to avoid any negative numbers when the microprocessor is doing A/D conversion.
Active Low Pass Filter
Circuit will perform low pass filtering to block any high frequencies from interfering with the EEG recording.

## Slide 33: Bluetooth Module and Battery
Arduino Wireless Bluetooth Module
Sends all digital information to the android application
35mA connecting 8mA paired
Polymer Lithium Ion Battery
Powers the arduino board,circuit,and bluetooth module
850mAh 3.7V
Place 2 in series to achieve 7.4V in order to power arduino
LiPo Charger Basic
Charges the battery after completion
Contains status LED and micro-usb connector
Charges 500mAh. Takes 1 ½ hours to charge

## Slide 34: Android Device
2013 Nexus 7
Android 4.4 (KitKat)
Android vs Apple
Tablet vs Mobile Phone

## Slide 35: Android Application
Development – Eclipse
Built in Android SDK
Coding – Java
Emulator
Alarm system
Data stored on internal Memory

## Slide 36: Design Overview
Electrodes
Isolation Amplifiers
Microcontroller
Battery and Signal Communication

## Slide 37: Budget

## Slide 38: Goals for Spring Semester
3D print headset
Complete full assembly
Methods for electrode placement
Create circuit and casing
Develop Android application
Testing for proper, comfortable fit and function

## Slide 39: Conclusion
Success of the EMD will be based it being:
Efficient
Effective
  Seizure detection
Low-Cost
  Increases availability
Easy to Use
  Intuitive controls
Portable
Wireless

## Slide 40: Epileptic Monitoring Device
Final Design Presentation – December 4 2013
Mark Curran (CE), Rachel Kolb (BME), Kevin Pineda (BME), & Timothy Skinner (EE)
Primary Advisor: Dr. Brett BuSha Secondary Advisor: Dr. Ambrose Adegbege

## Slide 41
Questions?
Comments?
Concerns?